## Simulations
In order to establish the capability of the analyzed methods of detrending on (1) the efficiency in removing the trend, (2) the capacity to detect the existing oscillations, and (3) the tendency to generate spurious oscillations, we carried out a series of numerical simulations. The analyzed methods of detrending included two families of procedures: the FIR based methods and the linear model (LM) based methods. The first family included rolling mean (k = 20) and FIR filter (B = [0.0606, 0.0675, 0.0731, 0.0773, 0.0798, 0.0807, 0.0798, 0.0773, 0.0731, 0.0675, 0.0606]). The latter family included linear and polynomial (fourth degree) regression. The detrenders from the LM family were implemented using a dedicated R package (detrendeR, https://github.com/bartekkroczek/detrendeR). The code of the simulations is available for download from .
The FIR family is local. It means that the there exist a distance from given moment in time, data beyond which do not affect a current trend estimation. On the other hand, the LM family is global – the entire dataset affects the whole trend estimation. Because of this difference the two families differ in their working when zero-padding is applied. While the FIR family is marginally affected by the zero-padding, the working of the LM family may be extremely sensitive to this process. For the above reason, and because we find the zero-padding process redundant in most cases, we tested the working of the detrenders from the LM family with the zero-padding and with the padding removed. (The padding was applied similarly as in every other method, but the padded samples were not taken into account when estimating the trend.)
We sampled one hundred accuracies for each of one thousand virtual agents with no individual differences. The data were sampled for one second (so the sampling rate was 100 Hz). The samples were drawn from an uniform distribution (minimum accuracy: .6, maximum: .9) and added the trend and optionally the target oscillations. The trend was either slow (.5 Hz) or fast (1.5 Hz) and had an amplitude of 0.03; the target oscillations had frequency of 6 Hz and amplitude of 0.014. Both types of oscillations had sinusoidal shape and random phase, individual for each agent.
The simulation parameter values were either selected as large values to meet all reasonable expectations as to the reliability of the simulations predictions (number of agents, number of samples, time of sampling), based on the values found in the literature (frequencies of the oscillations), or set arbitrarily (amplitudes of the oscillations and the uniform distribution boundaries). The values in the last group were chosen in order to show all possible effect in similar and intuitively plausible scale. The choice of these values did not affect the manifestation of the effects which occur for all values of these parameters in their neighboring ranges.
After generation each signal was preprocessed similarly to Chen et al. (2017) Song et al. (2014). The prepossessing included normalization, possible outliers removal (0 removed), zero-padding (50 samples before and 50 after signal), and Hanning tapering. After that the detrending processes were applied. Next, the zero-padding was removed and the signal was fast Fourier transformed. Finally the data were aggregated over agents.
We performed four simulations: with and without the target oscillations, and with slow and fast trend oscillations (0.5 Hz and 1.5 Hz). Depending on the detrending method we observed three phenomenons in the frequency domain: (1) the removal or lack of it of the trend, (2) the emergence or lack of it of the spurious oscillations, and (3) the detection of the target oscillations. The faultless detrending method should lead to the removal of the trend and detection of the target oscillations. It also should not induce emergence of spurious oscillations.
The Figure [TS1] presents the comparison of working of all the analyzed detrending methods. As one can see the polynomial method with the zero-padding removal is the only one that satisfy the goals of the proper detrending method. Other methods fail in one way or another. While all methods detect existing target oscillations, both the FIR filter and rolling mean generates spurious oscillations. The LM family methods does not fall for this trap but besides the method mentioned above they do not always remove the trend efficiently. The linear model does not remove the trend at all, while both the linear model with zero-padding removal and the polynomial method do remove the slow trend but fails to remove the fast trend. When no detrending method is used the spurious oscillations do not appear but the trend is not removed. Note that both FIR methods give larger estimation of the target oscillations, compared to no detrending, which probably means that their estimation is biased by the additional spurious component.
[Insert Figure TS1 here.]
Figure [TS1] caption: Fast Fourier transformed signal (power in the domain of frequency) from four simulations: without target oscillations (left panels) and with the target oscillations (right panels); with the slow trend oscillations (0.5 Hz, upper panels) and with fast trend oscillations (1.5 Hz, lower panels). Six methods of detrending and no detrending are compared (line types and colors, LM – linear model, PM – polynomial model). Three types of oscillations were observed (peaks marked with letters): trend (A), spurious oscillations (B), and target oscillations (C).

## Empirical Results
### Methods
### Results
The empirical data were analyzed using two methods established in the literature as tools for detecting possible oscillations. Both methods use Fourier-transformed data. The first one is a comparison (using ANOVA, linear model or similar tools) between values in the range of frequencies in which the peak is observed/expected and the values outside of the range (e.g., Mathewson et al., 2009). The second uses permutation (of time or accuracy labels) in order to estimate the distribution of results under the null hypothesis and then determining the significance of the effect on the base of this distribution (e.g., ).
Before using these two methods of statistical inference we preprocessed the data. The preprocessing included normalization, outliers removal (over 4 SDs from mean), Hanning tapering, and deterending, so it was similar to the one described in the Simulations section but without zero-padding. We did not zero-pad the data because the number of time points was sufficient to perform the analysis without this step and, more importantly, we consider zero-padding as a process which leads to possible artifacts and corruption of results.
We used two methods of detrending: one belonging to the FIR based family – a FIR filter (vector B was identical to the one used in the simulations), and second belonging to the LM family – a polynomial function (third degree). These two methods together with two above mentioned methods of statistical analysis gave, in effect, four comparable outcomes.
The first of two method of analysis included visual appraisal of both the peak in power (equivalent with dominant oscillations in a specific frequency range) and the margin of cutoff (stemming from removing low frequency trend, compare figure TS2). Second, we fit a mixed linear model with power as an explained variable, frequency range as a predictor, and participant as a source of random effect on slope. In the data detrended with the FIR filter the range of peak appeared to be [2.5 Hz, 6 Hz] while in the polynomial detrended data the range was [5 Hz, 8 Hz]. In both analyses we cut off data below 2.5 Hz due to its low power (see Figure TS2).
The second method included estimating the null hypothesis distribution and comparing observed power for each frequency to this estimated distribution. The test was directional (we expected the peak to exceed the non-peak values) and we used α of .05. Due to large number of comparisons (one for each of 24 frequencies) we report both raw and Holm adjusted p values. The null hypothesis distribution was estimated by shuffling time labels of the data in order to remove all possible time structure and processing the shuffled data as described above. The shuffling and processing was repeated 10000 times, giving a distribution which would be expected if no oscillations in accuracy occurred.
Among these four ways of preprocessing and analysis only the one based on FIR filter and mixed linear model showed statistically significant peak (B = 0.053, p = .017, marginal R2 = .0042, conditional R2 = .043). The same method of analysis performed on the polynomial-detrended data revealed no significant peak (p = .26, marginal R2 = .00087, conditional R2 = .04, see Figure TS2).
[Insert Figure TS2 here.]
Figure [TS2] caption: Fast Fourier transformed empirical data (power in the domain of frequency) detrended with the FIR filter (left panel) and polynomial function (right panel). In both cases the peak (round points) and cutoff margin (square points) were detected visually ex ante statistical test. The peak was compared to the background power. Asterisks mark a statistical significance on .01 level.

The effects of the same two preprocessing techniques were provided to a permutational analysis. This time the peak was not predefined but all values of power were compared against null hypothesis distribution. The confidence intervals and p-tests were directional (the peak could only exceed non-peak values). No power value for either FIR filter or polynomial function detrended values was significantly higher than a value expected under the null hypothesis. Figure TS3 presents the estimated power and the upper limit of null hypothesis distribution. Table TTS1 presents the results of the p-test.
[Insert Figure TS13 here.]
Figure [TS3] caption: Fast Fourier transformed empirical data (power in the domain of frequency) detrended with the FIR filter (left panel) and polynomial function (right panel). Solid lines represents observed mean power, shaded areas represent directional (upper constrained) 95% confidence intervals of null hypothesis. Note the fact that FIR filter based preprocessing induces spurious oscillations in the confidence intervals.

Table TTS1.: / Estimated power values and results of directional p-test (both raw and Holm adjusted) for each observed frequency (Hz) based on the permutational analysis
	FIR filter detrended			Polynomial function detrended
Frequency	Estimate	p	p†	Estimate	p	p†
0	0.086	.85	> .99	0	.38	> .99
1.277	0.435	.3	> .99	0.092	.46	> .99
2.553	0.612	.99	> .99	0.523	.77	> .99
3.83	0.661	.76	> .99	0.483	> .99	> .99
5.106	0.603	.1	> .99	0.536	.57	> .99
6.383	0.537	.82	> .99	0.572	.091	> .99
7.66	0.573	.95	> .99	0.536	.56	> .99
8.936	0.554	.96	> .99	0.503	.93	> .99
10.213	0.542	.75	> .99	0.496	.96	> .99
11.489	0.602	.23	> .99	0.503	.93	> .99
12.766	0.59	.74	> .99	0.522	.75	> .99
14.043	0.595	.28	> .99	0.538	.51	> .99
15.319	0.555	.65	> .99	0.543	.43	> .99
16.596	0.639	.054	> .99	0.534	.58	> .99
17.872	0.607	.35	> .99	0.551	.3	> .99
19.149	0.535	.91	> .99	0.531	.61	> .99
20.426	0.548	.86	> .99	0.557	.22	> .99
21.702	0.601	.47	> .99	0.564	.15	> .99
22.979	0.592	.41	> .99	0.546	.37	> .99
24.255	0.516	.44	> .99	0.505	.91	> .99
Note: Estimate – estimated mean power in given frequency, p† - Holm adjusted p-value.

## References
Mathewson, K. E., Gratton, G., Fabiani, M., Beck, D. M., & Ro, T. (2009). To see or not to see: prestimulus alpha phase predicts visual awareness. The Journal of Neuroscience: The Official Journal of the Society for Neuroscience, 29(9), 2725–2732. doi.org/10.1523/JNEUROSCI.3963-08.2009